ESP Hardware
Overview
5/8/22 Brent Roman brent@mbari.org

---
2G ESP Machine Types
- shallow
  - 50 meter rated can
  - All but one 2G ESP is of this type
- 4km
  - 4000 meter rated titanium sphere
  - Only one ever deployed
- mfb
  - standalone microfluidic block
    - affectionately named “tombstone”
    - still supported, but not none deployed

---
3G ESP Machine Types
- auv
  - Includes cartridge carousel
  - Suitable for deployment in MBARI Long-Range AUV
- portable
  - Single cartridge
  - Used for protocol development in lab

---
ESP Hardware Architecture
- Distributed control
  - All “work” delegated to microcontrollers
    - 2G calls them “dwarves”, 3G “elves”
  - All dwarf/elf microcontrollers are identical
    - all communicate on a shared I2C bus
    - all run the same firmware
  - The unique “gateway” microcontroller
    - connects the Linux Host Computer
      (via an RS-232 serial port)
    - to the microcontrollers’ common I2C bus

---
2G ESP Hardware Connectivity
SD
Card
Linux Host
Computer
RS-232
Can
Sensors
Gateway
Microcontroller
Shared I2C bus
Power
Switches
In 3G ESP architecture
“Elf” replaces “Dwarf” below
Processing
Dwarf
Manipulator
Dwarf
Collection
Dwarf
Storage
Dwarf
Sampler
Dwarf
Almost all ESP activity is funneled through the RS-232 link between Gateway and Linux Host
The Linux host may be replaced with any computer with a serial port (for lab testing)
Failures on any Microcontroller may cause I2C bus errors on others
Gateway failures may also be reported as I2C bus errors
RS-232
Serial
RS-232
Serial
Ethernet
RS-232
Console
3 Contextual
Sensors
3 Analytical
Modules

---
Simulated Hardware
- Can run in simulated time or real-time
- Each Simulated Dwarf or Elf
  - Implemented as a separate Ruby thread
    - while real microcontrollers are programmed in ‘C’
  - Responds to the exact same I2C bus messages
  - Models basic, linear motor and heater physics
    - Simulates “crash” if one attempt to run past end stop
    - However, does not model two actuators colliding
    - Heaters do not model boiling water
- In real-time, may be combined with real contextual sensors on RS-232 ports

---
Simulation Limitations
- Can environment is unchanging
- Energy Use is not tracked
- Filter clogging is not simulated
  - samples at constant rate until goal reached
  - one can set this simulated filtering rate
- No images generated
- No email messages in simulated time
  - But you can get emails running real-time sims
- Run your simulated time sims on a laptop
  - >100x faster than the ESP!